## Slide 1: Air Dispersion Modeling
Jeff Stonesifer, Meteorologist
March 10, 2020

## Slide 2: purpose
Using Air Dispersion Modeling
Models estimate impacts of pollution emitted by industry
Compare the estimated impacts to air quality standards
Air quality standards limit emissions from industry

## Slide 3: Permitting
Connection to Permitting
Modeling used to set permit conditions
  Require control strategies
  Hours of operation
  Emission rates
  Distance of equipment from fence

## Slide 4: Analogy
Sprinkler system surrounded by buckets
Wind is important in distributing water
Depth of water in buckets ~ concentrations at receptors
Notes: Sprinkler image: https://commons.wikimedia.org/wiki/File:Sprinkler_Irrigation_-_Sprinkler_head.JPG
Bucket image: https://www.google.com/imgres?imgurl=https%3A%2F%2Fblog.gunassociation.org%2Fwp-content%2Fuploads%2F2018%2F06%2Frain-falling-bucket-full-waterrainwater-harvestingrainy-rainwater-ss-Featured.jpg&imgrefurl=https%3A%2F%2Fblog.gunassociation.org%2Ffilter-rainwater%2F&tbnid=f-Jc0BiO1pbsKM&vet=12ahUKEwiXhtD1otPuAhUGlJ4KHUm9BS8QMygfegUIARD1Aw..i&docid=TxHjt4sM5yPBiM&w=1500&h=840&q=buckets%20collecting%20water&hl=en&ved=2ahUKEwiXhtD1otPuAhUGlJ4KHUm9BS8QMygfegUIARD1Aw

## Slide 5: inputs
Dispersion Model Inputs
WIND PROFILE
VORTEX
Building
CENTERLINE
Meteorology
Wind speed
Wind direction
Temperature
Sources
Source type
Parameters
Emissions
Rates
Hrs of operation
Terrain & Land Use
Rural or urban
Elevations
Gravitational Settling
Particle Size
Density
Downwash
Buildings

## Slide 6: Source type
Point Source

## Slide 7: Source type
Volume Source

## Slide 8: Guidelines
Federal, State, & Local Guidelines
Federal: 40 CFR 51, a.k.a. Appendix W
NMED’s Air Dispersion Modeling Guidelines
Air Quality Program’s Air Dispersion Modeling Guideline

## Slide 9: Cumulative impacts
Cumulative Impacts Modeling
Background levels are from monitored data
Background data added to modeled impact
Inclusion of nearby facilities depends on
  Distance from applicant’s facility
  Amount of emissions from nearby facilities
  What the background monitor is sampling

## Slide 10: Example
Recent modeling review
Albuquerque Asphalt HMA
Albuquerque Asphalt aggregate plant
D&R Tank

## Slide 11: example
NO2 model for the same facility

## Slide 12: Cumulative impacts
More on cumulative modeling
“…the question of which nearby sources to include in the cumulative modeling is inextricably linked to the question of what the ambient monitoring data represents within the project area.” –Section 8.3.3(a), p. 5221
Cumulative impact is compared to air quality standards

## Slide 13: compliance
Compare to Standards
NAAQS | Modeled Impact (µg/m3) | Background (µg/m3) | Model + Background (µg/m3) | Level of the standard (µg/m3)
NO2 1-hour | 117.1 | 62.8 | 179.9 | 188
PM10 24-hour | 65.7 | 35 | 100.7 | 150

## Slide 14: EPA Model
AERMOD
U.S. EPA’s preferred air dispersion model since Nov. 2005
Standard among all regulatory clean air agencies
Confidence that AERMOD doesn’t underestimate
  EPA is concerned about underestimation
  LOWWIND options have not been accepted for regulatory modeling

## Slide 15: Reliability
AERMOD Reliability
EPA SCRAM website
Databases used to evaluate AERMOD performance
Documents on AERMOD performance and formulation
Support Center for Regulatory Atmospheric Modeling (www.epa.gov/scram)
Notes: For more info: https://www.epa.gov/scram/air-quality-dispersion-modeling-preferred-and-recommended-models#aermod

## Slide 16: Verification
Example of EPA Testing AERMOD
Excerpts from description of EPA experiment:
  “…near-surface, non-buoyant tracer release” experiments with “surface sampling arrays positioned 50 meters to 800 meters downwind…”
Empire Abo, NM field study mentioned in
March 1, 2011 EPA clarification memo

## Slide 17: Safety
Furthering the Margin of Safety
Rural dispersion coefficients
Continuous full bore operations for all sources on property
Lack of NO2/NOX data  often results in worst-case assumptions

## Slide 18: Rejections
Reasons EHD Rejects Modeling
Discrepancy between model & application
  E.g. Application requests operations 7 days/wk; only modeled 6 days a week
Inappropriate modeling techniques
  Outdated downwash algorithm
  Inappropriate use of urban dispersion
Incorrect modeling
  Sources, roads, fence don’t match up with aerial imagery

## Slide 19: example
Example of Incorrect Mapping

## Slide 20: conclusion
In Conclusion
AQP uses checklists for protocol reviews, preliminary reviews, final reviews, and peer reviews as a matter of quality assurance and quality control.
AERMOD- a reliable tool for keeping Bernalillo County within the standards for particulates, H2S, lead, NO2, SO2, and CO

## Slide 21: Questions?

## Slide 22: references
AERMOD User’s Guide, https://gaftp.epa.gov/Air/aqmg/SCRAM/models/preferred/aermod/aermod_userguide.pdf
AERMOD: Latest Features and Evaluation Results, EPA-454/R-03-003, June 2003, https://gaftp.epa.gov/Air/aqmg/SCRAM/models/preferred/aermod/aermod_mep.pdf
Guideline on Air Quality Models (aka Appendix W), https://www.epa.gov/sites/production/files/2020-09/documents/appw_17.pdf

## Slide 23: REFERENCES
Additional Clarification Regarding Applicability of Appendix W Modeling Guidance for the 1-hour NO2 NAAQS (EPA Clarification Memo, 01Mar2011), https://www.epa.gov/sites/production/files/2020-10/documents/additional_clarifications_appendixw_hourly-no2-naaqs_final_03-01-2011.pdf

## Slide 24: REFERENCES
City of Albuquerque Environmental Health Department Air Dispersion Modeling Guidelines, https://documents.cabq.gov/environmental-health/airquality/ADM/final%20COA%20Oct2019%20guidelines.pdf
New Mexico Environment Department Air Dispersion Modeling Guidelines, https://www.env.nm.gov/air-quality/modeling-publications/